SIGLINK TYPE G V1.0 14-Pin GPIO Specification
DPX25-948674

ID: DPX25-948674 / DATE: 25/05/2025 / DOC VERSION: 1.0 / AUTHORS: / 0x4248 / COPYRIGHTS: / © 2025 0x4248. Under the CC BY-SA 4.0 License. / © 2025 4248 Systems, a part of 0x4248. Under the CC BY-SA 4.0 License.	DESCRIPTION / SIGLINK Family type G version 1.0 14-Pin general purpose input output cable, female and male port specification. For use on integrated devices and developmental purposes on electrical hardware.

# Editors notes
# This is a work in progress document and not fully complete
# Overview
The SIGLINK Type G V1.0 specification defines the electrical, mechanical, and signal mapping characteristics of a 14-pin General Purpose Input/Output (GPIO) connector system. Designed for interoperability across integrated development platforms and modular electronics, the Type G cable supports both male and female port configurations.
This specification aims to promote a standardised wiring interface for embedded systems, prototyping boards, and digital control hardware. It enables consistent connection logic, clear signal expectations, and improved cross-device compatibility. The 14-pin layout includes a mix of digital I/O, power, and reserved lines for future expansion or vendor-specific use.
The SIGLINK Type G connector is optimised for compact devices and development tools where reliable low-voltage signalling is essential. It is suitable for low-speed control, LED drivers, switch inputs, sensor arrays, and other GPIO applications.
# Electrical Specification
This section of the documentation will go over the electrical specification of the SIGLINK Type M.
## Voltage and Current Ratings and Configurations
The SIGLINK Type M can be be configured in several ways. Firstly there is an analogue mode and a digital mode. The analogue mode can send low voltage analogue signals and the digital mode can have three states OFF, LOW and HIGH.
### Analogue Ratings and Configurations
An analogue signal can be sent trough any of the GPIO pins providing the voltage inputs are between 0V and 5V and the amperage is no more than 25mA. The below diagram shows the input and output voltage curve.